## Slide 1
Notes: Set up
Preconfigure app_manifest.json
Load https://featured.chat on a browser window and login with your Twitch account
Open https://github.com/gloveboxes/Azure-Sphere-Learning-Path/tree/master/samples/LearnTV/end_to_end_demo_avnet
Open https://cs110037ffe87b282f1.z23.web.core.windows.net/
Delete existing on sphere apps

## Slide 2: Building highly secure IoT Solutions with Azure Sphere, Azure RTOS, and IoT Central
David Glover | Microsoft | Cloud Developer Advocate
@dglover | linkedin.com/in/gloveboxes
Mustafa Saifee | Microsoft Student Ambassador
@immustu | linkedin.com/in/saifeemustafaq/
http://aka.ms/IOTOxford
Notes: Hello and welcome to the Building highly secure IoT Solutions with Azure Sphere, Azure RTOS, and IoT Central
My name is Dave glover, I’m a Microsoft Cloud Dev advocate, based in Sydney Australia with a focus on the Internet of Things It is also my great pleasure to introduce Mustafa one of our student ambassadors based in India
Mustafa would you like to tell us a bit about yourself?
Thank you Mustafa
Security is the biggest challenge facing the IoT industry
It is often overlooked in the rush to bring a new product to market.
Security should be at the heart of ever IoT discussion
Now this session builds on the Learn TV event we did last week
I’m going to assume you have a reasonable idea about IoT solutions and cloud gateways
So we’ll go through the first part a bit faster
And we are going to mix it up a bit and Add in Real Time support with Azure RTOS
Azure Sphere is our platform to build highly secure devices that are secure by default

## Slide 3: /learn
aka.ms/learn/iotcentral
Follow along on
Microsoft Learn
Notes: DAVE TO TALK ABOUT THIS
In partnership with Oxford University we developed the Microsoft Learn Azure Sphere modules
This presentation is in support of this module
This session builds on last weeks Building secure IoT Solutions with Azure Sphere and IoT Central
We will be going deeper on the Azure Sphere development side and show how you can integrate High level apps with a Azure RTOS Real Time application

## Slide 4: Q & A
Tweet us your questions
Use the hashtag #LearnTV
Notes: This session is live
Moderators standing by to help answer your questions
And I will do my best to keep an eye on the questions too

## Slide 5: Agenda
IoT security risks
Azure Sphere security
Creating an Azure IoT Central Application
Create an Azure Sphere app Securely stream data to IoT Central Remote control from IoT Central
Notes: Dave

## Slide 6: Lab scenario: Measuring a lab environment
Remote monitoring and control of a microbiology laboratory
Pressure
Temperature
Humidity
Light Control
Notes: Mustafa: Intro lab scenario
Suppose you're a scientist in a microbiology laboratory who is responsible for storing samples from tests. You want to build a system that monitors the environment around the laboratory equipment in real time. This system would monitor the following room conditions:
Pressure
Light
Temperature
Humidity
Previously these were recorded manually by the lab assistants using sensors at regular intervals. Manual recording of ambient conditions is a tedious job which is also prone to human error. Having any issues with the sensors would invalidate the tests performed in the Lab environment.
Maintaining the room conditions accurately is critical for managing the laboratory. The lab needs to maintain the right conditions to help you get more accurate results. Any variation in the conditions can affect the equipment temperature during the storage and manipulation of the samples, specimens, and lab equipment. This could impact the ability to produce the correct and stable results and can also have an economic impact on the organization.

## Slide 7
“When smart gadgets spy on you: Your home life is less private than you think”
“Industrial IoT to equip new era of corporate intruders coming in through devices”
Cyberattacks On IOT Devices Surge 300% In 2019, ‘Measured In Billions’, Report Claims
“The Lurking Danger of Medical Device Hackers”
“The IoT ransomware threat is more serious than you think”
“Hackers exploit casino’s smart thermometer to steal database info”
“Hacking critical infrastructure via a vending machine? The IOT reality”
“Webcam firm recalls hackable devices after mighty Mirai botnet attack”
Notes: It is rare for a day to go by without some headline related to IoT security
Baby monitors, Toys, robot vacuum cleaners being used to spy on families
Heart pacemakers and cars Hijacked
Cyber attacks on cities - New Orleans https://www.foxnews.com/tech/new-orleans-cyberattack-costing-city-close-to-1m
Mira generated 623 Gbps attack from the Mirai botnet in 2016.”
Thousands of infected IoT devices used in for-profit anonymity service
  Some 9,000 devices—mostly running Android, but also the Linux and Darwin operating Systems—have been corralled into the Interplanetary Storm
  https://arstechnica.com/information-technology/2020/10/thousands-of-infected-iot-devices-used-in-for-profit-anonymity-service
Attacks have social, economic, and reputation implications.
None of use want to build devices that have to be recalled because of security issues.

## Slide 8: Casino Fish Tank Attack
Criminals Hacked A Fish Tank To Steal Data From A Casino
Notes: M: yeah it is a great example where IoT security goes wrong
This is a great example where an IoT device was not used in the way it was intended
M: outro – hey dave can you tell me more about how Azure Sphere address security issues

## Slide 9: Mitigating Security Risks
Complex, Expensive, Ongoing
Notes: Next, I want to talk about approaches to mitigating security risks
As I’m sure you will appreciate, security is a journey
Getting security right is complex, expensive, highly specialised and ongoing
Attack vectors constantly changing and becoming more cunning
Microsoft has a long history building secure internet connected systems
We are applying those lessons to Azure Sphere

## Slide 10: The 7 properties of highly secured devices Is your device highly secured or does it just have some security features?
Hardware Root of Trust
Defense in Depth
Small Trusted
Computing Base
Dynamic
Compartments
Certificate-Based Authentication
Error Reporting
Renewable Security
https://aka.ms/7properties
Notes: Microsoft and the industry identified 7 properties to building highly-secure network connected devices.
I’m not going to go into each of these in any detail – see the link at bottom aka.ms/7properties
A Hardware root of trust identifies a device with unforgeable cryptographic keys protected by hw
Dynamic Compartments hw barriers between software components that prevent a security breach in one layer reaching another layer
Certificate-based authentication proven using Hardware Root of Trust cryptographic key to prove the identity of the device
Renewable security. The device software is automatically updated to correct known vulnerabilities or security breaches.
Failure Reporting A software failure, such as buffer overrun attack should be reported to cloud based failure analysis systems
Defense in Depth multiple layers of protection, each layer verifying the next layer is secure.
A Small trusted computing base, hw and sw, together to protect the device identity and enforce security policies.

## Slide 11: Azure Sphere 3 components implement the 7 properties
Azure Sphere certified Microcontroller (MCU), from our silicon partners, with built-in Microsoft hardware root of trust.
The Azure Sphere OS with ongoing updates creates a Microsoft-secured software platform
The Azure Sphere Security Service guards every Azure Sphere device.
It brokers trust, detects emerging threats, renews device security, and app reporting.
Notes: D: Talk about Azure Sphere
It Implements the 7 properties of secure systems - Secure by default – everything is locked down!
Azure Sphere is a new class of secured, connected, crossover MCUs.
It supports real-time processing alongside a high level secure OS.
Azure Sphere certified MCUs: Provide secure, dependable hardware root of trust.
Azure Sphere OS with ongoing updates create the secure IoT platform. Azure OS is a hardened version of embedded Linux.
Azure Sphere Security Service: It brokers trust, detects emerging threats, and renews device security
Build secure, internet connected solutions. Updated, controlled, monitored and maintained remotely.

## Slide 12: Azure Sphere Microcontroller Silicon Design
Multiplexed I/O
SPI
I2C
UART
I2S
TDM
PWM
GPIO
ADC
2 x ARM Cortex-M4F
for real time processing
Network Connection WiFi in first chips
FLASH
≥ 4MB
SRAM
≥ 4MB
ARM Cortex-A7
optimized for low power
Firewall
Microsoft
Pluton
Security Subsystem
Firewall
Firewall
Firewall
Firewall
Firewall
Cores highlighted in red are application cores
Notes: Let’s look at the Azure Sphere MCU design.
5 Core Microcontroller
Highlighted in red
2 x Real time cores
1 x High level core
It’s a Multi Core Microcontroller
2 x Cortex-M4F cores. Support for real-time, bare metal processing – Existing code, FreeRTOS, Tiny Machine Learning Models
Connectivity Core for Dual Band Wifi - shipping in first chips (other connectivity to follow)
The Pluton Security System Core responsible for implementing security policies
Firewalls – two-fold
  Silicon countermeasures to ensure that IO peripherals are only accessible by the core they are mapped
  Memory Management Unit ensure hardware enforced memory spaces
Cortex-A. Crossover processor. Shrunk to fit using 40nm fabrication techniques.
  Runs at 500mhz rather than typical 1.2ghz to give low power.
  Has full Memory management unit to provide virtualised memory addressing for software compartments.
Tightly couple memory (TCM) SRAM dedicated to each core and flash storage.
Packaged as a 2mmx12mm 164pin DR-QFN (Dual Row, Quad Flat, No-leads) package
Attestation is a mechanism for software to prove its identity.
MT3620 is a highly integrated single chip tri-core MCU designed to meet the requirements of modern, robust internet-connected devices. It leverages the Microsoft Azure Sphere security architecture to provide an unprecedented level of security to connected device manufacturers. For the lifetime of the device the Azure Sphere solution provides device authentication and attestation, supports remote over-the-air software updates to maintain security in the face of evolving attacks, and automates error logging and reporting. Please refer to the “Azure Sphere Platform Overview” document from Microsoft for more information.
MT3620 features an application processor subsystem based on an ARM Cortex-A7 core which runs at up to 500MHz. The chip also includes two general purpose ARM CortexM4F I/O subsystems, each of which runs at up to 200MHz. These subsystems were designed to support real-time requirements when interfacing with a variety of on-chip peripherals including UART, I2C, SPI, I2S, and ADC. They are completely general-purpose Cortex-M4F units which may be tailored to specific application requirements. On-chip peripherals may be mapped to any of the three end-user accessible cores, including the CA7.
In addition to these three end-user accessible cores, MT3620 contains a security subsystem with its own dedicated CM4F core for secure boot and secure system operation. There is also a Wi-Fi subsystem controlled by a dedicated N9 32-bit RISC core. This contains a 1x1 dual-band 802.11a/b/g/n radio, baseband and MAC designed to support both low power and high throughput applications without placing computational load on the user-accessible cores. MT3620 also includes over 5MB of embedded RAM, split among the various cores. There is a fully-integrated PMU and a real-time clock. Flash memory is integrated in the MT3620 package; see section 3.2 for ordering information. Please refer to the “Azure Sphere MT3620 Support Status” document from Microsoft for information about how much memory and which hardware features are available to enduser applications. Only hardware features supported by the Azure Sphere solution are available to MT3620 end-users.
TCM, Tightly-Coupled Memory is one (or multiple) small, dedicated memory region that as the name implies is very close to the CPU. The main benefit of it is, that the CPU can access the TCM every cycle. Contrary to the ordinary memory there is no cache involved which makes all memory accesses predictable.
The main use of TCM is to store performance critical data and code. Interrupt handlers, data for real-time tasks and OS control structures are a common example.
In computer security, a side-channel attack is any attack based on information gained from the implementation of a computer system, rather than weaknesses in the implemented algorithm itself (e.g. cryptanalysis and software bugs). Timing information, power consumption, electromagnetic leaks or even sound can provide an extra source of information, which can be exploited.
PMU = Power Management Unit
https://docs.microsoft.com/en-au/azure-sphere/product-overview/what-is-azure-sphere
https://d86o2zu8ugzlg.cloudfront.net/mediatek-craft/documents/MediaTek-MT3620-Product-Brief-PDFMT3620PBA4-0919.pdf

## Slide 13: Azure Sphere Developer Boards
There are multiple types of boards available to use
https://aka.ms/IoTBoards
Notes: M: Hey M, can you tell us about the Azure Sphere Boards – Dave to click on the url
M: to hand over to D
https://docs.microsoft.com/en-us/learn/modules/develop-secure-iot-solutions-azure-sphere-iot-hub/3-gpio-hardware-interfaces
There are multiple types of boards available to use; let's look at the first one.

## Slide 14
NetX DUO
A dual IPv4 and IPv6 and TLS stack
Filex
Embedded FAT File System
USBX
USB Host/Device Stack
GUIX and GUIX Studio
Complete UI application design environment
ThreadX
Real-Time Operating System (RTOS)
TraceX
Real Time, Graphical Event Trace Analysis
Azure RTOS
https://azure.microsoft.com/services/rtos/
Notes: Page 12 Azure RTOS contains the following run time components. Run time components are the software running on the microprocessors. These components are: ThreadX, NetX Duo, FileX, GUIX, USBX. The component names are self-explanatory. We also supply two host-based development tools. GUIX Studio is a host based GUI design tool. It allows designer to create screen layout. Once the design is done, GUIX Studio translates the design into source code that can be imported into GUIX. TraceX is another host-based tool. It is used to visualize system events.

## Slide 15
2K
Min Footprint

## Slide 16: Components needed
The components you'll need to know are:
Azure IoT Central (trial)
Azure Sphere
Azure Sphere SDK
Azure Sphere tenant
  You claim and can remotely manage your Azure Spheres
Update the Azure Sphere OS
Azure Sphere Security Service
Notes: The components you'll need to know are:
Azure Sphere SDK
Azure Sphere tenant
Azure Sphere OS
Azure Sphere Security Service – it delivers security updates

## Slide 17: Connecting the lab monitor to Azure IoT Central

## Slide 18
Azure IoT Central
Analytics, dashboards and visualization
Extensibilities (Flow, Dynamics, Webhooks, etc.)
Monitoring rules and triggered actions
Fully hosted and managed by Microsoft
Device connectivity and management
Risk-free trial with simplified pricing
No cloud development expertise required
Notes: Reduces the complexity of IoT solutions with a fully managed SaaS offering for customers and partners that enables powerful IoT scenarios without requiring cloud solution expertise.
Simplifies the development process and makes it easy and fast for customers to get started, making digital transformation more accessible to everyone.
Available along with our existing platform-as-a-service (PaaS) solution, Azure IoT Suite, which enables deep customization and full control.

## Slide 19: Azure IoT Central Building Blocks
Azure
IoT Hub
Azure IoT Plug and Play
Azure
Device
Provisioning
Azure
Time-Series Insights
Azure
IoT Central
Notes: It is a solution that is built on Azure IoT Hub, device provisioning services, Time Series Insights

## Slide 20: Demo Create an IoT Central Template
Notes: Just create the template using the JSON file

## Slide 21: Secure IoT with Azure Sphere, Azure RTOS and IoT Central
Azure Sphere MT3620
Cortex A7 Application core
Cortex M4 Real-time core
Inter-core
Message bridge
Azure RTOS ThreadX
Inbound Requests Thread
Environment Sensor Thread
Outbound Responses
High-level application
Request Environment Telemetry
Receive Telemetry forward to Azure IoT
Azure IoT Central
Notes: M: Ask Dave why would you run apps on multiple cores and in particular the Cortex M4 Real time core
Running time sensitive code –sensor depends on predictable timing
Scenarios include migrating existing code
Running FreeRTOS and Azure RTOS
Running Time Machine Learning models – for example voice activation

## Slide 22: Demo Stream telemetry to Azure IoT Central

## Slide 23: Control lab lights with Azure IoT Central Commands
Notes: Dave talk about remote control
Mustafa will be controlling the application from the Commands tab

## Slide 24: IoT Central Commands
Azure Sphere
Direct method LightControl handler function
Apply action
Direct method handler response
3
4
5
Azure IoT Hub
Invoke LightControl direct method
6
Method Request
Method Response
Azure IoT Central
Invoke LightControl Command
IoT Hub Direct Method API
Method Response
1
2
Notes: Dave to discuss

## Slide 25: Demo Lab light control with Azure IoT Central Commands
Notes: Dave to do the code – will put breakpoint
Mustafa – you will invoke the method
Dave- switch and step through
Tweet on to #LearnTV http://aka.ms/learn/iothub/demo

## Slide 26: Setting Lab Environment Sensor rate with Azure IoT Central Properties
Notes: D: Current the code sends a message to Iot hub every 5 seconds
But we want to change that
We are going to use device twins

## Slide 27: IoT Central Properties
Azure Sphere
Azure IoT Hub application
Device twin
sensor measure rate handler
Change sensor measure Rate
Report configuration
Update desired sensor measure rate
device twin
2
4
5
Azure IoT Hub Device Twin
3
Properties.Desired
Data
Properties.Reported
Data
Azure IoT Central
Update sensor
measure rate
Property
IoT Hub
Device Twin API
Query DT
1
6
Notes: Change the rate the sensor os measured

## Slide 28: Demo Setting Lab Environment Sensor rate Azure IoT Central Properties
Notes: Dave to do the code – will put breakpoint
Mustafa – you will invoke the method
Dave- switch and step through
Tweet on to #LearnTV http://aka.ms/learn/iothub/demo

## Slide 29: Knowledge Check

## Slide 30: Question 1
In the Azure Sphere ecosystem, which component is missing from the following list? - Azure Sphere SDK, Azure Sphere tenant, Azure Sphere OS
A) Azure Sphere API
B) Azure Sphere Security Service
C) Azure Sphere Security Key
Notes: Explanation: Azure Sphere Security Service is a key component of the Azure Sphere ecosystem

## Slide 31: Question 1
In the Azure Sphere ecosystem, which component is missing from the following list? - Azure Sphere SDK, Azure Sphere tenant, Azure Sphere OS
A) Azure Sphere API
B) Azure Sphere Security Service
C) Azure Sphere Security Key
Notes: Explanation: Azure Sphere Security Service is a key component of the Azure Sphere ecosystem

## Slide 32: Question 2
Your organization created an Azure Sphere tenant and then claims each of its devices into that tenant – what function does this accomplish?
A) So that you can manage those devices remotely and securely.
B) The tenant allows devices to communicate better with other tenants.
C) Your organization can name individual devices.
Notes: Explanation: The tenant allows you to manage devices remotely and securely.

## Slide 33: Question 2
Your organization created an Azure Sphere tenant and then claims each of its devices into that tenant – what function does this accomplish?
A) So that you can manage those devices remotely and securely.
B) The tenant allows devices to communicate better with other tenants.
C) Your organization can name individual devices.
Notes: Explanation: The tenant allows you to manage devices remotely and securely.

## Slide 34: Summary

## Slide 35: Summary
IoT Centrals surfaces IoT value fast
Security must be part of your IoT story
Azure Sphere delivers a highly secure IoT device platform
Secure by default with ongoing security updates
Notes: Using an application built around the Azure Sphere, you can securely capture data and send it to the cloud for additional purposes. You firstly configure the Azure Sphere Application to connect to Azure IoT and when you execute an application, it connects and transmits data to the cloud. You can monitor the data being sent on the Azure IoT. You can send specific commands from the IoT Central to the device to control the device parameters. It can also send alerts messages to inform the authorized person.
Consider the scenario of monitoring the environment parameters such as temperature, air pressure, humidity, and light within a laboratory setting. You want to build and automate a new solution within the lab. This solution will include the sensors deployed in the lab that will record the ambient environmental conditions and transmit them securely to the cloud.
Without the Azure Sphere-based application, you would need to manually record these conditions at regular intervals and keep a record of it. And any variation in the Lab environment can't be detected in real time. Using this solution, we'll have the ability to produce accurate and stable results in near real time.

## Slide 36: /learn
aka.ms/learn/iotcentral
Follow along on
Microsoft Learn

## Slide 37: Upcoming sessions Mark your calendar
Session name | Time | Location/online link
Create a DevOps Solution for Azure IoT Edge Devices | October 12 1:00 PM PDT | aka.ms/oxDevOps
Develop Secure IoT Solutions with Azure Sphere and IoT Hub | October 13 1:00 PM PDT | aka.ms/oxIoTHub
Cognitive Services with Azure IoT Edge | October 19 1:00 PM PDT | aka.ms/oxCog
Develop Secure IoT Solutions with Azure Sphere and IoT Central | October 20 1:00 PM PDT | aka.ms/oxIotCentral

## Slide 38: Q & A
Tweet us your questions
Use the hashtag #LearnTV
Notes: Moderators standing by

## Slide 39
David Glover | Microsoft | Cloud Developer Advocate
@dglover | linkedin.com/in/gloveboxes
Mustafa Saifee | Microsoft Student Ambassador
@immustu | https://www.linkedin.com/in/saifeemustafaq/
Notes: My name is Dave glover, I’m a Microsoft Cloud Dev advocate, based in Sydney Australia with a focus on the Internet of Things It is also my great pleasure to introduce Mustafa one of our student ambassadors based in India
Thank you Mustafa
Security is the biggest challenge facing the IoT industry
It is often overlooked in the rush to bring a new product to market.
Security should be at the heart of ever IoT discussion
Now this session builds on the Learn TV event we did last week
I’m going to assume you have a reasonable idea about IoT solutions and cloud gateways
So we’ll go through the first part a bit faster
And we are going to mix it up a bit and Add in Real Time support with Azure RTOS
Azure Sphere is our platform to build highly secure devices that are secure by default

## Slide 41: Azure Sphere Developer Boards
There are multiple types of boards available to use
https://docs.microsoft.com/en-us/learn/modules/develop-secure-iot-solutions-azure-sphere-iot-hub/3-gpio-hardware-interfaces
Notes: M: Hey M, can you tell us about the Azure Sphere Boards – Dave to click on the url
M: to hand over to D
https://docs.microsoft.com/en-us/learn/modules/develop-secure-iot-solutions-azure-sphere-iot-hub/3-gpio-hardware-interfaces
There are multiple types of boards available to use; let's look at the first one.

## Slide 42: Secure IoT with Azure Sphere, Azure RTOS and IoT Central
Azure Sphere MT3620
Cortex A7 Application core
Cortex M4 Real-time core
Inter-core
Message bridge
Azure RTOS ThreadX
Environment telemetry service thread
Environment telemetry sense thread
High-level application
Request Environment Telemetry
Receive Telemetry forward to Azure IoT
Azure IoT Central
IoT Hub & Device Twins
DPS
ASA
TSI
Notes: M: Ask Dave why would you run apps on multiple cores and in particular the Cortex M4 Real time core
Running time sensitive code –sensor depends on predictable timing
Scenarios include migrating existing code
Running FreeRTOS and Azure RTOS
Running Time Machine Learning models – for example voice activation